## Slide 1
ITN 101
Reference Network
3-Tier Architecture | HSRP Redundancy | Wireless
Brightpoint Community College | BET Division | Spring 2026

## Slide 2
3-Tier Lab Rack Topology
CORE
DIST
ACCESS
Internet
R1 - ISR 4221 Core | HSRP Active VL10/40
R2 - ISR 4221 Core | HSRP Active VL20
HSRP
SW-DIST — Catalyst 1000 Distribution Layer (L2 Backbone) | VLANs 10, 20, 40, 99 trunked
trunk
WAP-1
VLAN 40
SW-ACC — Cat 2960 Access Layer
PC-A
VL10
PC-B
VL10
PC-C
VL20
SRV-1
VL30
WAN
10.0.1.0/30
R3 - ISR 1941
Branch | Serial labs
BRANCH
Legend: --- WAN — Trunk ■ VL10 ■ VL20 ■ VL30 ■ VL40 ● HSRP

## Slide 3
HSRP Redundancy & Load Balancing
Both routers carry traffic. Neither sits idle.
VLAN 10 — Students
192.168.10.0/24
Virtual GW: .1 (Virtual GW)
R1: .2 / Active (110)
R2: .3 / Standby (100)
VLAN 20 — Faculty
192.168.20.0/24
Virtual GW: .1 (Virtual GW)
R1: .3 / Standby (100)
R2: .2 / Active (110)
VLAN 40 — Wireless
192.168.40.0/24
Virtual GW: .1 (Virtual GW)
R1: .2 / Active (110)
R2: .3 / Standby (100)
Key: Hosts always use .1 (virtual IP). If the active router fails, the standby promotes within ~3 seconds. Preemption restores the original active when it recovers.

## Slide 4
IP Addressing at a Glance
VL10 — Students
192.168.10.0/24
GW (HSRP): .1
R1: .2 | R2: .3
VL20 — Faculty
192.168.20.0/24
GW (HSRP): .1
R2: .2 | R1: .3
VL30 — Servers
192.168.30.0/24
GW: .1 (R3)
DNS: .10
VL40 — Wireless
192.168.40.0/24
GW (HSRP): .1
R1: .2 | R2: .3
WAN Link
R2 ↔ R3 (Simulated T1)
10.0.1.0/30
R2 G0/0/1: .1 | R3 G0/1: .2 | bandwidth 1544 (T1 sim)
Management: 172.16.0.0/24 R1: .1 | R2: .2 | R3: .3 | SW-D: .11 | SW-A: .12 | AP: .20
R3 Serial Ports: S0/0/0 and S0/0/1 (HWIC-2T) available for dedicated serial WAN lab exercises

## Slide 5
Protocol Roles & Services
HSRP
R1 + R2
Load-balanced:
R1 active VL10/40
R2 active VL20
DHCP
R1 + SRV-1
R1: VLANs 10/20/40
SRV-1: VLAN 30
Pools: .100-.199
DNS
SRV-1
192.168.30.10
All pools point here
NAT (PAT)
R1
Overload on G0/0/0
for internet access
OSPF
R1, R2, R3
Area 0
R2 = campus-branch
transit
NTP
R1 (master)
Stratum 4
All devices sync

## Slide 6
Simplified Reference — The Mental Model
Patterns to Memorize
3rd octet = VLAN ID
VL10→10.x | VL20→20.x | VL30→30.x | VL40→40.x
HSRP virtual gateway = .1
Active router = .2, Standby = .3
Load-balanced HSRP
R1 active for VL10/40, R2 active for VL20
WAN link = /30 mask
Only 2 usable IPs (one per router end)
3-Tier: Core → Dist → Access
Route at core, trunk at dist, assign VLANs at access
Quick Reference
Network | Subnet
Students (VL10) | 192.168.10.0/24
Faculty (VL20) | 192.168.20.0/24
Servers (VL30) | 192.168.30.0/24
Wireless (VL40) | 192.168.40.0/24
WAN R2↔R3 | 10.0.1.0/30
Management | 172.16.0.0/24
Troubleshooting Order:
1. Ping own IP (NIC/stack)
2. Ping HSRP virtual GW (.1)
3. Ping DNS (192.168.30.10)
4. Ping public IP (8.8.8.8)
5. nslookup google.com